Password Based Circuit Breaker with Overload Protection using GSM

ABSTRACT

The project is designed to control a circuit breaker with help of a password only. A keypad is connected to the project to enter the password. Fatal electrical accidents to the line man are increasing during the electric line repair due to the lack of communication and co-ordination between the maintenance staff and the electric substation staff.

This proposed system provides a solution, which can ensure the safety of the maintenance staff e.g. line man. The control to turn ON/OFF the line lies with the line man only. This system has an arrangement such that a password is required to operate the circuit breaker (ON/OFF). Line man can turn off the supply and comfortably repair it, and return to the substation, then turn on the line by entering the correct password.

The system is fully controlled by a microcontroller from 8051 family. A matrix keypad is interfaced to the microcontroller to enter the password. The entered password is compared with the password stored in the ROM of the microcontroller. If the password entered is correct, then only the line can be turned ON/OFF. Activation / deactivation of the circuit breaker is indicated by a lamp (ON/OFF). Overload Protection is also used in the project. In this project GSM modem is interfaced for remotely controlling the circuit breaker via SMS.

BLOCK DIAGRAM

# Text boxes

Microcontroller

LCD 16X2

Current Transformer

CT Circuit

Contactor

Relay

Keypad

GSM Module

Load

Reset & Crystal Circuit